## Slide 1: HALMAC Write IO Offload
yclin6797

## Slide 2: Design Goal
Reduces USB registers latency in time restrictions scenario. Ex. Scan channels
Prevents from HW issues host & FW accesses CMAC registers at the same time

## Slide 3: Outline
Overview
  Overview Flow
  Event Notifications
Write IO Offload in Detail
  API & Input Parameters
  Flow Chart
  Return Values
  Macros in halmac

## Slide 4
Overview

## Slide 5: Overview Flow
Write IO offload 是把 1 至數個 IO 合併到一個 H2C 內、FW 收到 H2C 後執行 H2C 內的 IO。
下完 H2C 後、會用 Busy Waiting 的方式 Polling FW 是否完成；同時禁止其他 function 執行 Write IO offload，以避免 Race condition。
  Polling period: 50us、polling count: 1000。共 Polling 50 ms。
  Flow 如下:

## Slide 6: Event Notifications
MSG_EVT_DATA_PATH_START & MSG_EVT_DATA_PATH_STOP
  為了避免讀寫 Registers 造成的 Latency、有兩種方式可 Polling FW: Registers & C2H packets
  收到 MSG_EVT_DATA_PATH_START: 用 C2H packets polling
  收到 MSG_EVT_DATA_PATH_STOP & 預設: 用 Registers polling
MSG_EVT_SURPRISE_REMOVE
  因為 Polling FW 時間長達 50ms，避免 Driver 發生 Surprise remove 後還在 Polling 導致 Driver 無法退出，收到 MSG_EVT_SURPRISE_REMOVE 後會停止 Polling

## Slide 7
Write IO Offload in Detail

## Slide 8: API & Input Parameters
API: add_cmd_ofld
Parameters:
  struct mac_ax_adapter *adapter: halmac adapter
  struct rtw_mac_cmd *cmd:
    enum rtw_mac_cmd_type_ofld type
      RTW_MAC_WRITE_OFLD: write register
      RTW_MAC_COMPARE_OFLD: polling register
      RTW_MAC_DELAY_OFLD: delay specific us
    enum rtw_mac_src_cmd_ofld src
      RTW_MAC_BB_CMD_OFLD: 0x1861000 ~ 0x1861FFFF
      RTW_MAC_RF_CMD_OFLD: RF registers
      RTW_MAC_MAC_CMD_OFLD: 0x1860000 ~ 0x1860FFFF
    enum rtw_mac_rf_path rf_path: RF path A~D
    offset: the register offset according to src
    mask: write/polling mask
    value: write/polling value. The value is SHIFTED value.
    ls: 1: send H2C with aggregated IOs to FW. 0: temporally save IOs
    id: currently, the field is NOT used.

## Slide 9: Flow Chart

## Slide 10: Return Value
Value | Description
MACBADDR | Offset 不為 4-byte alignment
MACNOFW | 沒有 FW
MACPROCERR | 其他 Function 正在使用 IO offload API. 建議 Retry 或者依序 halmac APIs
MACNPTR | Null pointer
MACNOBUF | Fail to set H2C buffer
MACPOLLTO | Polling FW timeout
MACFIOOFLD | IO offload FAIL
MACDRVRM | Surprise remove
MACBUFALLOC | Malloc fail

## Slide 11: Macros in halmac (1/2)
To simplify the code flow, there are some macros in halmac.
MAC_REG_W8_OFLD(offset, val, lc): write 8-bit value
  offset: MAC REG offset
  val: 8-bit val to be written
  lc: is last IO or not
MAC_REG_W16_OFLD(offset, val, lc): write 16-bit value
  offset: MAC REG offset
  val: 16-bit val to be written
  lc: is last IO or not
MAC_REG_W32_OFLD(offset, val, lc): write 32-bit value
  offset: MAC REG offset
  val: 32-bit val to be written
  lc: is last IO or not

## Slide 12: Macros in halmac (2/2)
MAC_REG_W_OFLD(offset, mask, val, lc)
  offset: MAC REG offset
  mask: mask value to be written
  val: 32-bit val to be written
  lc: is last IO or not
MAC_REG_P_OFLD(offset, mask, val, lc)
  offset: MAC REG offset
  mask: mask value to be written
  val: 32-bit val to be written
  lc: is last IO or not
DELAY_OFLD(val, lc)
  val: delay period in us
  lc: is last IO or not